## Slide 1: Agent Development (Decision Making, Behavior and Control)

## Slide 2
Player Structures (Implementations)

## Slide 3: Player Structures
Player functionality can be implemented several ways
  Composite: components attached to a generic Player class
  Subclass: a new derived Player implements functionality
  Mixture: partial implementation of functionality in subclass
Composite
Subclass
Combination: Subclass and Composite

## Slide 4: Composite Structure
General purpose interface to those sub-systems
from Player.h
“Aero model” for aircraft

## Slide 5: Aero Model: Generalized 6-DOF
Autopilot
Engine(s)
Control
Surfaces
Coefficients
Lift
Drag
Side
Roll
Pitch
Yaw
Flight
Control
System
Forces
And
Moments
EOM
F = m*a
Wt & CG
Aircraft
State
Ground
Reactions
Pilot
Features and capabilities of FCS and Autopilot vary. Because of that, different “layers” of control exist.

## Slide 6: FCS / Autopilot / FMS Relationships (Wikipedia Definitions)
Flight Control System (FCS)
  The direct (mechanical or fly by wire) connection between pilot stick and throttle inputs to aerodynamic surfaces
Autopilot
  System used to guide or control a vehicle without assistance from a human being
  Often an integral component of a Flight Management System
Flight Management System (FMS)
  FMS controlled through a CDU
  Guide aircraft along with flight plan, includes navigation database, waypoints, routes, etc
Example FMS Control Display Unit (CDU)
Saitek X52 Flight Control System
Functionality of each system component is not always this clear cut.

## Slide 7: Layers of Functionality
Fight Control System
Autopilot
Fight Mgt System
“Control”
Pilot
“Behavior”
“Decision Making”

## Slide 8: Layers of Functionality
Simple player dynamics
  Position and simple movement
Stick & throttle control
FCS / Autopilot
Pilot Interface
  AutoPilot

## Slide 9
Simple Player Dynamics

## Slide 10: Simple Player Dynamics
Every Player can do the following
  Set position
    North/East/Down (NED) (x, y, altitude)
    Geodetic (lat, long, altitude)
    Geocentric (ECEF) (x, y, z)
  Set roll, pitch & heading
  Initial velocity
    Player has a built-in dynamics model for simple movement
Simple player dynamics model useful for testing

## Slide 11: Stick & Throttle Control (assumes DynamicsModel or Subclassing)

## Slide 12: Composite Structure
General purpose interface to those sub-systems
from Player.h
Required

## Slide 13: Player FCS Interface
from Player.h

## Slide 14: Player FCS Interface
Default: requires a DynamicsModel to do anything meaningful
Functionality can be implemented in subclass
from Player.cpp

## Slide 15: Input File Example

## Slide 16: Human Input to Player
Stick & Throttle Inputs Arrive Here

## Slide 17: Player w/DynamicsModel
Player may or may not have an attached dynamics model
If attached, then stick and throttle inputs are forwarded to the dynamics model
Physics

## Slide 18: Subclassed Player
Stick and throttle functionality implemented in subclass

## Slide 19
Flight Control System (FCS) / Autopilot
(Higher level commands/control)

## Slide 20: Composite Structure
General purpose interface to those sub-systems
from Player.h
Must contain an auto pilot

## Slide 21: Player FCS / Autopilot Interface
Player interface to FCS / Autopilot is driven by “commands”
from Player.h

## Slide 22: Player FCS / Autopilot Interface
from Player.cpp

## Slide 23: Player FCS / Autopilot Interface
Player may or may not have an attached dynamics model
If attached, then stick and throttle inputs are forwarded to the dynamics model – some dynamics models do not include an autopilot!
If overridden in subclass, subclass will receive inputs
May or may not include autopilot
Includes an autopilot

## Slide 24
Pilot Interface (Not associated with a DynamicsModel)

## Slide 25: Composite Structure
General purpose interface to those sub-systems
from Player.h

## Slide 26: Pilot
NOT part of DynamicsModel!
General interface class to implement pilot decision logic
Base pilot class does nothing interesting, AutoPilot class adds functionality

## Slide 27: AutoPilot
Behavior
Control
AutoPilot complements the functionality of the FCS/Autopilot by providing higher level features (e.g., Flight Management System level capabilities)
Called in each frame (process phase)
As currently defined, it doesn’t make “decisions”

## Slide 28: AutoPilot
Behavior (e.g., follow routes,
loiter, follow another player)

## Slide 29: Navigation
AutoPilot uses Navigation
  Navigation contains routes, which contain steerpoints
  Steerpoints can contain Actions!

## Slide 30: Example Input File
RacModel has a auto pilot within its dynamic model
Auto pilot that follows the defined route within navigation system
Attached navigation system that includes a defined route

## Slide 31: Example Input File
Steerpoints define position and desired airspeed, etc

## Slide 32: Steerpoint Actions
Steerpoint can have an associated Action
  Examples: Take SAR image, release weapon, release decoy, etc

## Slide 33: Flow of Decisions and Actions
AutoPilot determines “high level” things to do, and how to do it via commands to “FCS / Autopilot” or even through direct control in some cases
Onboard computer could also be used to perform related functions

## Slide 34
Pilot Structures (Implementations)

## Slide 35: Pilot Structures
Pilot functionality can be implemented several ways
  Direct subclassing (e.g., AutoPilot, UBF Agent, etc)
  Indirect interface to external software system (e.g., Soar, CLIPS, scripts, etc)
Decision Making
Behavior
Control

## Slide 36: EOF