## Slide 1: Player Agent (Decision Making, Behavior and Control)
Douglas D. Hodson 3 March 2013

## Slide 2: Player Control – Layers of Functionality
Simple player dynamics
  Basic functionality
Advanced player dynamics
  Direct stick input
  Autopilot functionality
Pilot
  AutoPilot

## Slide 3
Player Structures (Implementation of Functionality)

## Slide 4: Player Structures (Implementation)
Player functionality can be implemented several ways
  Composite: components attached to a generic Player class
  Subclass: a new derived Player implements functionality
  Mixture: partial implementation of functionality in subclass
Composite
Subclass
Subclass and Composite

## Slide 5: Composite Structure
General purpose interface to those sub-systems
from Player.h

## Slide 6: Generalized 6-DOF Aero Model
Autopilot
Engine(s)
Control
Surfaces
Coefficients
Lift
Drag
Side
Roll
Pitch
Yaw
Flight
Control
System
Forces
And
Moments
EOM
F = m*a
Wt & CG
Aircraft
State
Ground
Reactions
Pilot
Features and capabilities of the autopilot vary. Because of that, different “layers” of control exist.

## Slide 7: FCS / Autopilot / FMS Relationships
Flight Control System (FCS)
  The direct (mechanical or fly by wire) connection between pilot stick and throttle inputs to aerodynamic surfaces
Autopilot
  System used to guide a vehicle without assistance from a human being
  Often an integral component of a Flight Management System
Flight Management System (FMS)
  FMS controlled through a CDU
  Guide aircraft along with flight plan, includes navigation database, waypoints, routes, etc
Example FMS Control Display Unit (CDU)
Saitek X52 Flight Control System
Functionality of each system component is not always this clear cut.

## Slide 8
Simple Player Dynamics (DynamicsModel not required)

## Slide 9: Simple Player Dynamics
Every Player can do the following
  Set position
    North/East/Down (NED) (x, y, altitude)
    Geodetic (lat, long, altitude)
    Geocentric (ECEF) (x, y, z)
  Set roll, pitch & heading
  Initial velocity
    Player has a built-in dynamics model for simple movement
Simple player dynamics model useful for testing

## Slide 10: Direct Stick Input (assumes DynamicsModel or Subclassing)

## Slide 11: Composite Structure
General purpose interface to those sub-systems
from Player.h
Required

## Slide 12: Direct Stick Input
from Player.h

## Slide 13: Direct Stick Input
Requires a DynamicsModel to do anything meaningful
Functionality can be implemented in subclass
from Player.cpp

## Slide 14: Input File Example

## Slide 15: Human Input to Player
Stick & Throttle Inputs Arrive Here

## Slide 16: Player w/DynamicsModel
Player may or may not have an attached dynamics model
If attached, then stick and throttle inputs are forwarded to the dynamics model
Physics

## Slide 17: Subclassed Player
Stick and throttle functionality implemented in subclass

## Slide 18
Dynamics Model Autopilot (assumes DynamicsModel or sub-classing that includes an autopilot)

## Slide 19: Composite Structure
General purpose interface to those sub-systems
from Player.h
Must contain an auto pilot

## Slide 20: Dynamics Model Autopilot
Player interface to DynamicsModel autopilot is driven by “commands”
from Player.h

## Slide 21: Dynamics Model Autopilot
from Player.cpp

## Slide 22: Dynamics Model Autopilot
Player may or may not have an attached dynamics model
If attached, then stick and throttle inputs are forwarded to the dynamics model – some dynamics models do not include an autopilot!
If overridden in subclass, subclass will receive inputs
May or may not include autopilot
Includes an autopilot

## Slide 23
Pilot (Not associated with a DynamicsModel)

## Slide 24: Composite Structure
General purpose interface to those sub-systems
from Player.h

## Slide 25: Pilot
NOT part of DynamicsModel!
General interface class to implement pilot decision logic
Base pilot class does nothing interesting, AutoPilot class adds functionality

## Slide 26: AutoPilot
Behavior
Control
AutoPilot complements the functionality of the DynamicsModel autopilot or subclassed Player features (Flight Management System level capabilities)
Defined functionality is called in each frame (process phase)
As currently defined, it doesn’t make decisions

## Slide 27: AutoPilot
Behavior (e.g., follow routes,
loiter, follow another player)

## Slide 28: Navigation
AutoPilot uses Navigation
  Navigation contains routes, which contain steerpoints
  Steerpoints can contain Actions!

## Slide 29: Example Input File
RacModel has a auto pilot within its dynamic model
Auto pilot that follows the defined route within navigation system
Attached navigation system that includes a defined route

## Slide 30: Example Input File
Steerpoints define position and desired airspeed, etc

## Slide 31: Steerpoint Actions
Steerpoint can have an associated Action
  Examples: Take SAR image, release weapon, release decoy, etc

## Slide 32: Flow of Decisions and Actions
AutoPilot determines “high level” things to do, and how to do it via commands to “dynamic model auto pilot” or even direct control in some cases
Onboard computer could also be used to perform related functions

## Slide 33
Pilot Structures (Implementation of Functionality)

## Slide 34: Pilot Structures (Implementation)
Pilot functionality can be implemented several ways
  Direct subclassing (e.g., AutoPilot, UBF Agent, etc)
  Indirect interface to external software system (e.g., Soar, CLIPS, etc)
  Maybe a scripting system
Decision Making
Behavior
Control

## Slide 35: EOF